| REF No: | NTET RA-RSB1 | ACTIVITY: | RACK SAW BENCH DEMONSTRATION |
| --- | --- | --- | --- |

| DETAILS of TASK/OPERATION BEING ASSESSED |
| --- |
| Name of Event |  |
| Location |  |
| Date of Assessment |  | Assessed by |  |

PURPOSE/METHOD OF WORK

It is essential for the Operator to understand the correct procedures and familiarise him/herself with the machine before starting work. 1) Obtain the material to be cut 2) Place material on to a suitable work surface 3) Ensure machine is running correctly 4) Start task 5) Carry out the task 6) On completion of tasks stop blade from rotating 7) Clean the saw with a soft hand brush NOTE When possible use a mobile feeder as it reduces the risks of coming into contact with the blades. Use fences and a push-stick in order to keep your hands away from the blades. A push-stick should always be used when making any cut less than 300mm in length or when feeding the last 300mm of a longer cut. The leading hand should never be closer than is necessary to the front of the saw and hands should never be in line with the saw blade. A push-stick should always be used to remove the cut piece from between the saw blade and fence. (Only when blade is stationary) Do not use the circular saw to cut rebates or grooves or perform tenoning jobs. Avoid making blind or interrupted cuts. Ensure blades/cutting tips are kept sharp Keep blade free from saw dust or other waste materials WARNING Never use the saw bench with safety devices removed or out of order Do not leave the saw bench unattended while it is running Never remove safety guards (top or bottom) from the saw bench

| SPECIFIC LEGISLATIVE REQUIREMENTS |  | LEVEL OF SKILL/TRAINING REQUIRED |
| --- | --- | --- |
| HASAW Act 1974 Management of Health and Safety at Work Regulation 1999 PUWE Regulation 1998 Manual Handling Regulation 1992 Safe Use of Work Equipment Provision and Use of Work Equipment Regulations 1998 as applied to woodworking Code of Practice for Safety of Machinery 1999 Safety of Woodworking Machines Management of Health and Safety at Work Reg. 1992 (MHSW) COSHH Reg Simple Guide for Provision & Use of Work Equipment 1998 Lifting Equipment Regulations 1998 (LOLER) Control of Noise at Work Regulation 2005 |  | All persons involved in operations should receive appropriate training and information regarding the specific control measures. Only operators who have been authorised as being fully trained and competent should be allowed to operate machines. Training in shut down procedures Manual Handling Refresher training should be carried out on a regular basis. |

| CHEMICALS/MATERIALS INVOLVED | RA NO. | ASSESSMENT DATE |  | SPECIFIC WORK EQUIPMENT PROVIDED |
| --- | --- | --- | --- | --- |
| Wood dusts – hard/soft | N/A |  |  | Soft hand brush, dust masks, goggles |

| MAIN HAZARDS IDENTIFIED | WHO WILL BE AFFECTED | CONTROL MEASURES TO REDUCE THE RISK |
| --- | --- | --- |
| 1. Changing of Blade | Demonstrator Crew | Compliance with acknowledged procedures |
| 2. Vibration | Demonstrator Crew | A safe system of working should be implemented. |
| 3. Noise | Demonstrator Crew | Ear defenders should be worn by those closest to source of noise. |
| 4. Dust/splinters | Demonstrator Crew | Operatives to wear eye protection, facemask and overalls. A suitable restricted area for crew around the saw should be marked. Public should not be allowed in the area when the bench is in operation. |
| 5. Cuts from handling timber | Demonstrator Crew | Wear gloves when moving and lifting timber. |
| 6. Strains/sprains from lifting/carrying timber | Demonstrator Crew | Carry out manual handling assessment. Basic Manual Handling training for operatives. Seek assistance with heavy/awkward loads. If possible when handling awkward or heavy sections may need to break/dismantle into manageable pieces. Use mechanical aids where possible for transporting materials. |
| 7. Slips and trips | Demonstrator Crew | Ensure good housekeeping at workplace is maintained to practical health and safety standards. Keep floor around work area free of oil, grease and wood shavings/sawdust. Ensure that materials are stored within the allocated/demarcated areas to avoid encroaching onto walkways, etc. |
| 8. Eye injury/eye irritation | Demonstrator Crew | Wear eye protection where eye injury likely i.e. to protect against splinters and cuts. Avoid contact with lubricants. |
| 9. Skin irritation | Demonstrator Crew | Avoid contact with lubricants. Wear gloves when handling irritants Good hygiene principles i.e. wash hands before eating, drinking and after work is completed |
| 10. Foot injury | Demonstrator Crew | Wear safety footwear if risk of penetration/injury, incorporate mid-sole protection. |
| 11. Fire | Demonstrator Crew | Ensure good housekeeping. NO SMOKING. Ensure that all crew are aware of the fire procedures in place. Ensure appropriate fire extinguisher available to hand when carrying out work |
| 12. General | Demonstrator Crew | Control/restrict access to workplace |
| 13. Contact with Blade | Demonstrator Crew | All guards and riving blade to be in place |
| 14. Contact with open drive belt | Demonstrator Crew | Restrict access to belt area where possible. Ensure practical Health & Safety standards are maintained |
| 15. Inclement Weather | Demonstrator Crew | Stop/limit demonstration |